PRODUCT  SPECIFICATION

1.PRODUCT  CODE     BELS37104

2. DESCRIPTION        3 Core Flat Twin  and earth 2 x7/1.04  ( 6 mmsq.) plus 1 x 7/.67 (2.5mmsq) 			           P.A.C.W. HFI-90-TP  insulated  and HFS-90-TP sheathed .

Low Smoke Zero Halogen .

Building Cable 450/750 volt to AS5000.2 .

Oxygen Free Copper . RoHS Compliant .

3. CONSTRUCTION

3.1 CONDUCTORS

PHASE:  7  strands  of  1.04 mm  Plain  Annealed  Copper  to

AS1125  drawn  from  Class  102  copper  to

AS1574.

Max.  D.C. resistance  at  20C  :  3.08 ohms / km

3.2 		   EARTH  :  7  strands  of  0.67 mm  Plain  Annealed  Copper  to

AS1125  drawn  from  Class  102  copper  to

AS1574.

Max.  D.C. resistance  at  20C  :  7.41 ohms / km

3.3INSULATION :

ACTIVE and NEUTRAL   : Coloured  HFI-90-TP. to  AS3808 .

Nominal  Diameter  :  4.8mm

Nom.  Wall  Thickness:  0.8mm

EARTH   : Coloured  HFI-90-TP. to  AS3808 .

Nominal  Diameter  :  3.4mm

Nom.  Wall  Thickness:  0.7mm

3.3  CORE  COLOURS

ACTIVE   1. Red    NEUTRAL 2 . Black

EARTH    3. Lt Green / Yellow

Laid  parallel.

3.4  SHEATH         :    Coloured  HFS-90-TP  to  AS3808

Flat  configuration

Nominal  Dimensions  : 7.0 x 15.3  mm

Nom.  Wall  Thickness  : 1.1  mm

IDENTIFICATION

Printed on  the sheath

TYCAB  2009  ELECTRIC CABLE  HFI-90-TP  450/750V - BELS37104   LSOH    6 MM2 T + 2.5MM2 E